## Slide 1: Probabilistic Omnidirectional Path Loss Models for Millimeter-Wave Outdoor Communications
Mathew K. Samimi, Theodore S. Rappaport, and George R. MacCartney, Jr.
Polytech. Sch. of Eng., Wireless Res. Center, NYU, New York, NY, USA
Hong Cheng
chenghong@kw.ac.kr
Advisor: Prof. Hyukjoon Lee
Computer Intelligence Network Laboratory, Dept. of CE, KwangWoon University
IEEE Wireless Communications Letters ( Volume: 4, Issue: 4, Aug. 2015 )

## Slide 2: Previous Work
INTRODUCTION
Fitting a minimum mean square error (MMSE) best ﬁt line to the measured path losses (with distances in log- scale), yielding a mathematically-based omnidirectional path loss model, applicable over the range of measured distance
Floating-intercept Model
Arising from electromagnetic theory
using a constraint anchor point at the close-in reference distance d0 (assuming free space propagation up to d0) when ﬁtting the MMSE best ﬁt line, where the slope of the best ﬁt line and standard deviation beyond d0 are commonly known as the path loss exponent (PLE) and shadowing factor, respectively.
Close-in Free Space Reference Distance Model

## Slide 3: Works In The Paper
We present omnidirectional path loss models based on the same new york city data from both line-of-sight (LOS) and non-line-of-sight (NLOS) locations,
But consider a site-specific function that describes the probability of having a LOS path for a given transmitter-receiver (T-R) separation distance.
In this new “hybrid” path loss model, the mean estimated path loss is probabilistic.
INTRODUCTION

## Slide 4: Obtained the LOS probabilities
PROBABILITY OF LOS
Fig. 2. LOS probability curves from ray-tracing as a function of T-R separation distance for TX locations
As the T-R separation distance increases from 10 m to about 30 m, the probability of LOS remains constant with a value of 100%
And it decreases monotonically after 30 m, as the environment becomes denser with more path obstructions.
The mean LOS probability was computed from the four distinct LOS probability curves from the four physical TX locations used in [3] and [4].
The mean LOS probability curve was fit to an analytical function.

## Slide 5: Obtained the LOS probabilities
PROBABILITY OF LOS
dBP is the breakpoint distance at which the LOS probability is no longer equal to 1,
α (m) is a decay parameter.
In this work, we applied the minimum mean square error (MMSE) method, which yielded values of dBP = 27 m and α = 71 m that minimize the mean square error between the mean LOS curve in Fig. 2 and (1)
Other cities and environments will likely have different values of dBP and α , based on the density of buildings, the width of streets, and the heights of TX and RX antennas.

## Slide 6: Obtained the LOS probabilities
Simulation
clear
clc
d= 1:1:200 ;
d_BP = 27;
alpha = 71;
d0 = 1;
c = 3*10^8;
P_LOS = zeros(200,1);
for d=1:1:200
P_LOS(d) = (min(d_BP/d,1)*(1-exp(-d/alpha))+exp(-d/alpha))^2;
end
t = 1:1:200;figure;axis([0,100,1,200]);
plot(t,P_LOS*100,'r--','LineWidth',2);
lgd=legend('\fontsize {12}MMSE Fit');
lgd.FontWeight = 'bold';
xlabel('T-R Separation(m)','FontSize',12,'FontWeight','bold')
ylabel('LOS Probability(%)','FontSize',12,'FontWeight','bold')
grid on;
https://matlab.mathworks.com/

## Slide 7: Measurements Parameters
PROBABILISTIC MODEL
A fixed reference distance of d0 = 1 m , and the probability of LOS shown in (1).
The LOS and NLOS path loss equation lines are of this form :
PLLOS is the LOS free space path loss

## Slide 8: Measurements Parameters
PROBABILISTIC MODEL
PLNLOS,Close−In and PLNLOS,Floating are the NLOS path losses computed using the 1 m close-in free space reference distance and the floating-intercept models, respectively,
λ is the carrier wavelength
are the average (over distance) path loss exponents in LOS and NLOS, respectively·
α and β are the intercept and slope of the floating-intercept model parameters
Xσ is the lognormal random variable (normal in dB) with standard deviation σ (dB) to model largescale shadowing. lognpdf(d,mean,variance)

## Slide 9: Measurements Parameters
PROBABILISTIC MODEL
Statistic and Machine Learning Toolbox
https://cn.mathworks.com/products/statistics/

## Slide 10: Measurements Parameters
PROBABILISTIC MODEL

## Slide 11: Measurements Parameters
PROBABILISTIC MODEL

## Slide 12: Measurements Parameters
PROBABILISTIC MODEL
The omnidirectional LOS path loss exponent and shadowing factor with respect to a 1 m free space reference distance were computed to be
nLOS = 2.1 and σLOS = 3.6 dB at 28 GHz
nLOS = 2.0 and σLOS = 4.8 dB at 73 GHz
For the NLOS，
nNLOS = 3.4 and σNLOS = 9.7 dB at 28 GHz
nNLOS = 3.4 and σNLOS = 7.9 dB at 73 GHz
The NLOS floating-intercept path loss equation lines produced the following parameters
α = 79.2 dB, β = 2.6 and σNLOS = 9.6 dB at 28 GHz
α = 80.6 dB, β = 2.9 and σNLOS = 7.8 dB at 73 GHz

## Slide 13: Measurements Parameters
PROBABILISTIC MODEL
Figs. 3 and 4 show the 28 GHz and 73 GHz omnidirectional path loss scatter plots and corresponding mean path loss equation lines,
Using Eqs. (3), (4), and (5), in conjunction with (1), it is possible to implement a general probabilistic path loss model,
where PLOS(d), PLLOS(d), and PLNLOS(d) are given in Eqs. (1), (3), and (4) or (5),

## Slide 14: Measurements Parameters
PROBABILISTIC MODEL

## Slide 15: Measurements Parameters
PROBABILISTIC MODEL

## Slide 16: Measurements Parameters
Simulation
clear
clc
d= 1:1:200 ;
d_BP = 27;
alpha = 71;
d0 = 1;
c = 3*10^8;
Lambda =c/f ;
P_LOS = zeros(200,1);
PL_LOS = zeros(200,1);
PL_NLOS = zeros(200,1);
PL_Prob = zeros(200,1);
PL_NLOS_CloseIn = zeros(200,1);
PL_NLOS_Floating = zeros(200,1);
f = 28*10^9;
n_LOS = 2.1;
Sigma_LOS = 3.6;
n_NLOS = 3.4;
Sigma_NLOS = 9.7;
alpha2 = 79.2;
Beta = 2.6;
Sigma2_NLOS = 9.6;
https://matlab.mathworks.com/

## Slide 17: Measurements Parameters
Simulation
for d=1:1:200
P_LOS(d) = (min(d_BP/d,1)*(1-exp(-d/alpha))+exp(-d/alpha))^2;
PL_LOS(d) = 20*log10(4*pi/ Lambda)+10*n_LOS *log10(d)+lognpdf(d,0,Sigma_LOS );
PL_NLOS_CloseIn(d) = 20*log10(4*pi/ Lambda)+10*n_NLOS *log10(d)+lognpdf(d,0,Sigma_NLOS );
PL_NLOS_Floating(d) = alpha2 +10* Beta *log10(d)+lognpdf(d,0,Sigma2_NLOS );
if d<= 30
PL_NLOS(d) = PL_NLOS_CloseIn(d);
else
PL_NLOS(d) = PL_NLOS_Floating(d);
end
PL_Prob(d) = P_LOS(d)*PL_LOS(d)+(1-P_LOS(d))*PL_NLOS(d);
PL_Prob_CloseIn(d) = P_LOS(d)*PL_LOS(d)+(1-P_LOS(d))*PL_NLOS_CloseIn(d);
PL_Prob_Floating(d) = P_LOS(d)*PL_LOS(d)+(1-P_LOS(d))*PL_NLOS_Floating(d);
end

## Slide 18: Measurements Parameters
Simulation
figure;t = 1:1:50;%in fact it should be 30
s1 = semilogx(t,PL_LOS(1:50),'b-','LineWidth',2);grid on;hold on;
t = 31:1:200;%in the paper it begin at 51
p1 = plot(t,PL_NLOS_Floating(31:200),'r-','LineWidth',2);
t = 1:1:200;
p2 = plot(t, PL_NLOS_CloseIn,'r--','LineWidth',2);
p3 = plot(t,PL_Prob_Floating,'k-','LineWidth',2);
p4 = plot(t,PL_Prob_CloseIn,'k--','LineWidth',2);
axis([1,250,55,150]);
xlabel('T-R Separation(m)','FontSize',12,'FontWeight','bold')
ylabel('Total Path Loss (dB)','FontSize',12,'FontWeight','bold')
title('28GHz Omnidirectional Path Loss Models','FontSize',12,'FontWeight','bold')
grid on;
t1 = 'n_L_O_S=2.1 \sigma_L_O_S=3.6dB';
t2 = ['(\alpha _N_L_O_S, \beta_N_L_O_S)=(79.2dB,2.6) ', sprintf('\n'), '\sigma_N_L_O_S=9.6dB'];
t3 = ['n_N_L_O_S=3.4 \sigma_N_L_O_S=9.7dB'];
t4 = ['Probabilistic Path Loss (Floating)' ];
t5 = ['Probabilistic Path Loss (Close-In)' ];
line_handles = [s1,p1,p2,p3,p4];
legend_texts = {t1, t2, t3, t4,t5};
h_leg = legend(line_handles, legend_texts);
h_leg.FontWeight = 'bold';
h_leg.Location = 'best';

## Slide 19: Measurements Parameters
PROBABILISTIC MODEL

## Slide 20: Measurements Parameters
Simulation

## Slide 21: Measurements Parameters
PROBABILISTIC MODEL
are the mean LOS and NLOS distance-dependent path loss equations from Eqs. (3), and (4) or (5)
Xσ(d) is the sum of two independent 0 dB mean lognormal random variables, also with 0 dB mean
Distance-dependent standard deviation, i.e., shadow factor, (in dB)
It is clear that any other distance-dependent path loss model or other propagation models, could be used here .Eq. (6) can be rewritten as

## Slide 22: THANK YOU
Computer Intelligence Network Laboratory, Dept. of CE, KwangWoon University